Quaid-e-Azam Solar Power (Pvt.) Ltd.

15-Sep-2017

RFP for Remote SCADA Monitoring System Extension

Pre-Bid Clarifications Meeting (06-Sep-2017)

| Sr. No. | ITB Section | Query | Response |
| --- | --- | --- | --- |
| 1 | Section 4, item 5 | Sample Raw Data file to be shared with the bidders for better understanding. | Shared. |
| 2 | Section 4, item 7 | Please clarify what is the understanding of Company regarding Data Redundancy. Whether this redundancy is software redundancy or Hardware redundancy. | Redundancy is required. However, hardware for redundant software may be provided by the Company. Bidders are requested to share the specs of hardware clearly. |
| 3 | Section 4, item 8 | The SCADA System shall have modular functionality with 10% spare slots for easy extension in future. Please clarify whether Company require spare TAGs | 10% spare capacity includes the 10% spare tags. |
| 4 | Section 4, item 12 | String Comparison. Please clarify whether Company wants to have string comparison of Instantaneous Power only or the comparison shall be based on every parameter such as Power, Energy, Voltage, Current. | The string comparison includes the comparison of all values for 19,756 strings inclusive of Power, Energy, Voltage, Current. |
| 5 | Section 4, item 16 | Do Company requires a software with separate license for the monitoring in head office OR the workstation provided in Head Office shall be used of Web-View of the installed software as mentioned under item 5 of Technical specification. | It can be done through web-based interface. Also, we have separate public IP addresses and VPN available. Bidder should be able to set up web link/direct link head office without any additional cost. |
| 6 | Section 4, item 30 | Commissioning of NR Panels. Bidders require the contact details of NR Electric for coordination regarding the commissioning of NR Electric Panels | Name: Wang Gaole e-mail: wanggaole@nrec.com w184270085@qq.com |
| 7 | Financial Bid Form | Bidders raised queries about the impact of evaluation of annual license fees for project life time. | The financial bid form is updated and attached herewith. Bidders are request to fill the updated financial bid submission form. |